## Slide 1: A Rain Garden Rebate Program Save Barnegat Bay NEMO Program
Rutgers Cooperative Extension Water Resources Program
Chris Obropta

## Slide 2
Overview
What happens when it rains?
Statement of the problem
Existing development and impervious cover
The solution – rain gardens
The Rain Garden Rebate Program

## Slide 3
What happens to the rain in our watersheds?
It is absorbed by plants…
It infiltrates into soils…
It evaporates…
It runs off of rooftops and pavement…

## Slide 4
What is stormwater runoff?
Stormwater is the water from rain or melting snows that can become “runoff,” flowing over the ground surface and returning to lakes and streams.

## Slide 5: Statement of Problem
Stormwater runoff from existing development is destroying the health of our waterways and causing localized flooding.

## Slide 6
more development
More impervious surfaces
more stormwater runoff
10%
20%
30%
55%
The Impact of Development on Stormwater Runoff

## Slide 7: To minimize impact of stormwater runoff, you must control runoff from impervious surfaces

## Slide 8: Lots of impervious surfaces

## Slide 9
Connected or Disconnected?

## Slide 10: Part of the Solution
Install a rain garden

## Slide 11: Rain Gardens
A rain garden is a landscaped, shallow depression that is designed to capture, treat, and infiltrate stormwater at the source before it becomes runoff.
Notes: What is a rain garden?

## Slide 12
Notes: The Blue House Picture. Before and after a roadside rain garden. Talk about increasing property value!

## Slide 13: Parts of a Rain Garden

## Slide 14: Rain Gardens
  Landscaped areas that treat stormwater runoff
  Designed to merge two important goals: aesthetics and water quality
  Can be blended into the landscape and made to look natural
  Water is directed into them by pipes, swales, or curb openings
Notes: More about rain gardens.

## Slide 15: Site Selection
Next to a building with a basement, rain garden should be located at a minimum of 10′ from building; no basement, 2′ from building
Do not place rain garden within 25′ of a septic system
Do not situate rain garden in soggy places where water already ponds
Avoid seasonably-high water tables within 2′ of rain garden depth
Consider flat areas first – easier digging
Avoid placing rain garden within dripline of trees
Provide adequate space for rain garden
Notes: Siting considerations.

## Slide 16: Native Vegetation
Notes: We plant our rain garden with native plants.

## Slide 17
Notes: Can be incorporated into the landscapes of individual homes

## Slide 18: How do we get people to install rain gardens?
By providing incentives and technical assistance to homeowners
The Rain Garden Rebate Program

## Slide 19: Rebate Program Details
One educational session (45 minutes)
One-on-one technical sessions with designer (30 minutes per homeowner)
Leaves technical session with a plan
Rebates of $3 per square foot of garden or more
Inspections of completed gardens

## Slide 20: Educational Sessions
Photo courtesy of: NJWSA
Photo courtesy of: NJWSA
Photo courtesy of: NJWSA

## Slide 21
Take Home Handouts

## Slide 22: Check Your Soil Infiltration/Percolation Test
  Dig a hole in the proposed rain garden site (12” deep, 4-6” wide)
  Fill with water to saturate soil and then let stand until all the water has drained into the soil
  Once water has drained, refill the empty hole again with water so that the water level is about 1” from the top of the hole
  Check depth of water with a ruler every hour for at least 4 hours
  Calculate how many inches of water drained per hour

## Slide 26: Technical Support Sessions

## Slide 27: Rebate Program Summary
Must attend an educational workshop
  Attend a technical session with a rain garden designer
  Native plants are preferred. Installed plants must not be an invasive species
  Renters need a signed written agreement from the homeowner/property manager prior to participation
  Participants must pledge to maintain their rain garden for at least five (5) years

## Slide 28: Rebate Summary
All rain gardens installed must pass inspection
$3 per square foot of rain garden (some programs offer more)
up to $450 per property
Minimum size: 25 square feet

## Slide 29: Examples of Rebate Designs and Installations

## Slide 30: 125-Roof Runoff
Design
Installed Rain Garden

## Slide 31: 8-Roof, Sump Pump and Driveway Runoff
Design
Installed Rain Garden

## Slide 32: 966-Roof Runoff
Design
Installed Rain Garden

## Slide 33: 406-Driveway Runoff
Design
Rain Garden Installed

## Slide 34: 5-Driveway Runoff
Design
Installed Rain Garden

## Slide 35: 240-Roof Runoff
Installed Rain Garden
Design

## Slide 36: 23-Garage Roof Runoff and Rain Barrel Overflow

## Slide 37: Some Lessons Learned
Design assistance was a primary influence for individuals to install a rain garden not the rebate!
Local projects integrated into the educational program appears to increase participation (limit technical information and show examples!)
Need to find assistance for those unable to physically do it themselves

## Slide 38
Notes: 2013 Attendees

## Slide 39
Notes: 2014 Attendees

## Slide 41: Additional Resources

## Slide 42
Here is the website for the rain garden manual: http://www.water.rutgers.edu/Rain_Gardens/RGWebsite/RainGardenManualofNJ.html
Notes: We have a rain garden manual that is available for download from our website.

## Slide 43
Notes: We worked with UCONN to develop a rain garden app for New Jersey.

## Slide 44: Christopher C. Obropta, Ph.D., P.E. E-mail: obropta@envsci.rutgers.edu www.water.rutgers.edu