## Slide 1: Rain Gardens: A Simple Solution for Almost Any Existing Development Save Barnegat Bay NEMO Program
Rutgers Cooperative Extension Water Resources Program
Chris Obropta

## Slide 2
Overview
Directly Connected Impervious Surfaces
Disconnection with a Rain Garden
What is a Rain Garden and why you should want one?
Site Selection
Native Plants
Rain Garden Examples
Resources for you

## Slide 3
Keep the Rain from the Drain
Notes: This rooftop is directly connected to the street. The rooftop runoff flows to the road to the catch basin to the stream. This rooftop is directly connected to the stream.

## Slide 4: Disconnect with a Rain Garden
Notes: Disconnect the rooftop to a rain garden.

## Slide 5: Rain Gardens
A rain garden is a landscaped, shallow depression that is designed to capture, treat, and infiltrate stormwater at the source before it becomes runoff.
Notes: What is a rain garden?

## Slide 6
Parts of a Rain Garden
Notes: 6
A rain garden has a flat bottom and fills up with stormwater runoff that slowly seeps into the soil.
6

## Slide 7: Rain Gardens
  Landscaped areas that treat stormwater runoff
  Designed to merge two important goals: aesthetics and water quality
  Can be blended into the landscape and made to look natural
  Water is directed into them by pipes, swales, or curb openings
Notes: More about rain gardens.

## Slide 8: Site Selection
Next to a building with a basement, rain garden should be located at a minimum of 10′ from building; no basement, 2′ from building
Do not place rain garden within 25′ of a septic system
Do not situate rain garden in soggy places where water already ponds
Avoid seasonably-high water tables within 2′ of rain garden depth
Consider flat areas first – easier digging
Avoid placing rain garden within dripline of trees
Provide adequate space for rain garden
Notes: Siting considerations.

## Slide 9: Native Vegetation
Notes: We plant our rain garden with native plants.

## Slide 10
Notes: The Blue House Picture. Before and after a roadside rain garden. Talk about increasing property value!

## Slide 11
Notes: Volunteers building a rain garden at elementary school in Cranford, NJ

## Slide 12
Notes: Beautiful rain garden at the Fanwood Public Library

## Slide 13
Notes: The crescent moon rain garden at the Woodbridge Health Department

## Slide 14
Notes: A shady area can be perfect for a rain garden.

## Slide 15
Notes: More native plants.

## Slide 16
Notes: Provides wildlife habitat

## Slide 17
Notes: Are more aesthetically pleasing than conventional detention basins

## Slide 18
Notes: Can be incorporated into the landscapes of individual homes

## Slide 19
Notes: Sequesters carbon – nice addition to the parking lot

## Slide 20
Notes: Rain garden at the Hillsborough Municipal Building

## Slide 21
Here is the website for the rain garden manual: http://www.water.rutgers.edu/Rain_Gardens/RGWebsite/RainGardenManualofNJ.html
Notes: We have a rain garden manual that is available for download from our website.

## Slide 22
Notes: We worked with UCONN to develop a rain garden app for New Jersey.

## Slide 23: It is time to do your part
NJ’s waterways are polluted because of stormwater runoff from existing development
Stormwater runoff from existing development causes a majority of localized flooding
A rain garden is a very simple way everybody can help improve the health of our waterways and reduce localized flooding

## Slide 24: Christopher C. Obropta, Ph.D., P.E. E-mail: obropta@envsci.rutgers.edu www.water.rutgers.edu