## Slide 1: Manufactured Treatment Devices; A Stormwater Management Option for Urban Sites
Stephen J. Souza, Ph.D.

## Slide 2: Challenges Of Retrofitting Urban and Suburban Stormwater Systems
Lack of space for surface GI BMPs
Flashy flows
Inconsistent flows
Sediment, litter and trash
Specialized maintenance needs

## Slide 3: Manufactured Treatment Devices
Green/gray SW solutions
Sub-surface; decreases land availability requirements
Scalable
Often no need to make major changes to existing SW infrastructure
NJDEP accepted SW solution
Peak flow mitigation but limited recharge
Remove mostly particulate pollutants and TSS (50-80%) not much dissolved nutrient / pollutant removal

## Slide 4: MTD Utilization for New Development as per NJDEP
An MTD must be NJCAT verified and NJDEP certified if used to satisfy requirements for major development as per NJAC 7:8 (Stormwater Rules).
For projects receiving New Jersey Environmental Infrastructure Financing Program (NJEIFP) funding, an MTD must be either: 1) NJCAT verified and NJDEP certified or 2) installed as per the NJEIFP MTD Funding Policy.
An MTD not NJCAT verified or NJDEP certified may be used only if the MTD is not intended to satisfy the requirements of NJAC 7:8 and is not subject to NJEIFP MTD Funding Policy.
For list of qualifying MTDs and more details go to: https://nj.gov/dep/stormwater/treatment.html

## Slide 5: NJDEP’s Take on MTDs As Green Infrastructure Option
For an MTD to be considered by NJDEP as “green infrastructure”, the MTD must meet the NJAC 7:8-1.2 green infrastructure definition.
Specifically, the MTD shall (1) infiltrate into the subsoil; and/or (2) treat stormwater runoff through filtration by vegetation or soil.

## Slide 6: Use of MTDs in Barnegat Bay Watershed
Much of BB watershed developed before GI requirements and even basic stormwater management requirements of NJAC 7:8
Option for retrofit and redevelopment
Pre-treatment for GI SWM techniques
Illustration from:
Journal of Env. Engineering
Vol 144:2, 2018

## Slide 7: Variety of Designs and Applications

## Slide 8: Variety of Designs and Applications
Basin inserts and filter bags
Tree and planter boxes
Large chamber baffle boxes
Large chamber swirl condensers and hydrodynamic separators
Media filtration and cartridge filtration systems
Visit: https://nj.gov/dep/stormwater/treatment.html

## Slide 9: Flex Storm™ Catch Basin Inserts
Filter removes sediment, leaf litter, and other particulates
Treats runoff generated by 1-yr event and 1st flush of larger storms

## Slide 10: Catch Basin Inserts
Stainless steel frame adaptable to various size catch basins…
As per FlexStorm
Capable of 99% TSS removal @ flow rate of 137 GPM/Ft2
Filter bag capacity
5-6 Ft3

## Slide 11: Catch Basin Modification

## Slide 12: Catch Basin Clean Out

## Slide 13: Tree and Planter Boxes / Tree Trench
Filtration, assimilation of dissolved pollutants
and potentially some recharge

## Slide 14
https://wiki.sustainabletechnologies.ca/wiki/Stormwater_Tree_Trenches
Tree Trench

## Slide 15: Planter Boxes
Custom concrete boxes of variable size
Treats only small volume of runoff (1-year storm and 1st flush of larger storms)
Runoff diverted into boxes via pipe, weir or simple curb-cuts
Best when built with under-drain to prevent prolonged standing water
Fill with a bioretention soil mix
Plant with typical bioretention vegetation

## Slide 16: Example – Toms River HS North

## Slide 22: Tree Boxes
Source: https://www.townofmilton.org/stormwater-management/pages/tree-filter-boxes-milton
Source: University of New Hampshire, Stormwater Center. 2009 Biannual Report

## Slide 23: Tree Box Installation OCP, Lakewood
Tree Box 2
Tree Box 1
Discharge
Filterra™ Tree Boxes passively biotreat parking lot runoff that flowed unabated into Swimming Lake

## Slide 24: Filterra™ Tree Boxes OCP

## Slide 25: Filterra ™ Tree Boxes OCP

## Slide 26: Toms River HS North Filterra ™ Tree Boxes
Filterra tree box (91 ft²) installed in high school southwestern parking lot
Modify curb line to direct low flow into box
Planted with two 6-7 feet tall Serviceberry (Amelanchier canadensis)
Treated flow leaving Filterra unit discharged into a large sub-surface MTD for added flow management and TSS removal

## Slide 27
Retrofit of Existing Parking Lot Drainage System Toms River HS North

## Slide 28: Tree Box Retrofit of Existing Parking

## Slide 29: Large MTDs
https://www.conteches.com/stormwater-management/treatment/vortechs

## Slide 30: Large MTD – Toms River HS North
Vortechs 16000 MTD treats runoff exiting the Filterra unit plus additional parking lot runoff
The Vortechs 16000 is a hydrodynamic separator, combines swirl concentration and flow controls to trap and remove trash, debris, sediment, and hydrocarbons from runoff
The MTD discharges to existing stormwater system

## Slide 31
MTD Installed at Toms River HS North
Helical Swirl Condenser
Basin Baffles
Flow path

## Slide 32
MTD Installed at Toms River HS North

## Slide 33: Large MTD Installations Deal Lake, Asbury Park
Due to limited open space use both large and small subsurface MTDs to treat stormwater runoff…effective means of controlling floatables, sediment, particulate pollutants and nutrients…inspected quarterly and cleaned out

## Slide 34: Deal Lake – Comstock Ave, Asbury Park HS
Six-months of accumulated debris

## Slide 35: Other Deal Lake Installations
Debris and oil trapped after one storm

## Slide 36: Suntree ™ MTD
Achieved 8 tons of sediment removal w/in 4 months

## Slide 37: Summary
Although all MTDs are not “true” GI SWM solutions, they do treat runoff better than conventional gray SW techniques
Especially suitable for retrofit applications
Limited amount of land requirements
Installed without major alterations of existing infrastructure
Good for particulate pollutant and sediment removal

## Slide 38: Summary
Require frequent inspection and maintenance
Maintenance may require specialized equipment and trained personnel
Can only manage limited catchment area…OK for small volume of runoff
But, can be linked with GI SWM techniques or used as pre-treatment to increase pollutant removal

## Slide 39
Thank You…Questions
Stephen J. Souza, Ph.D.