## Slide 1: Importance of Riparian Buffers in Restoration of Barnegat Bay
Stephen J. Souza, Ph.D.

## Slide 2: What We’ll Cover
What's a riparian buffer? Legal and environmental definitions
The Ecological Functions (environmental benefits) of riparian buffers
The Ecological Services (societal benefits) of riparian buffers
Examples of riparian buffer restoration

## Slide 3: What We Won’t Cover
How to delineate a stream’s riparian buffer in accordance with the Flood Hazard Control Act Rules 7:13.
Various factors and conditions that define the width of the riparian buffer.
What activities are allowed within the riparian buffer and various enabling regulatory permits.

## Slide 4: EPA’s Definition of Riparian Area1
“Vegetated ecosystem along a waterbody through which energy, materials and water pass”.
  Combination of wetlands and uplands
  Includes floodplain and some transitional uplands
“Riparian buffer part of Riparian Area”…land adjacent to a stream.
A natural filter that removes various non-point source pollutants as well as mitigate flood related impacts.
USEPA 2005. National Management Measures to Protect and Restore Wetlands and Riparian Areas for the Abatement of Nonpoint Source Pollution. EPA 841-B05-003.
Tjaden and Weber 1998. Riparian Buffer Management, Fact Sheet 174, Maryland Cooperative Extension

## Slide 5: NJDEP Definition of Riparian Zone as per NJAC 7:13
A buffer adjacent to a surface water (streams, lakes, and rivers).
Varies in width…50, 150, or 300-ft wide along both sides of the waterway; width function of the waterway’s classification (NJAC 7:9B).
Almost every waterway that collects runoff from at least 50 acres of land possesses a riparian zone.
Any naturally occurring stream with a discernible channel possesses a riparian zone, no matter how small the area that drains to the stream.

## Slide 6: General Schematic of Stream, Flood Plain and Riparian Buffer
EPA 2010 – Guidance for Federal Land Management in the Chesapeake Bay Watershed, Chap 5, Riparian Area Management EPA841-R-10-002
Uplands
Uplands
Stream Channel
Flood Plain
Flood Plain

## Slide 7: Ecological Services and Functions
Ecological Services – Attributes that yield “societal/ cultural” benefits.
Ecological Functions – Attributes that yield “environmental or ecosystem” benefits.
Ecological services and functions of forested riparian buffers and headwater riparian buffers especially significant (Klapproth and Johnson. 2009. VPI, Publication 420-152 & Kaplan, et. al. 2008. Protecting Headwaters, Stroud Water Research Center)

## Slide 8: Ecological Services and Functions of Riparian Buffer
Services (Societal)
Flood mitigation and resiliency
Stream aesthetics
Passive recreation
Active recreation
Passive treatment of NPS pollution
Clean water
Functions (Environmental)
Nutrient assimilation
Stream corridor stability
Temperature control
Aquatic and semi-aquatic species habitat
Stream and wetland biodiversity
Organic material

## Slide 9: How Does A Riparian Buffer Function?
LGPC.ny.gov
Chesapeakebay.net

## Slide 10: Undisturbed Floodplain and Riparian Corridor
Riparian Corridor
Stream Corridor Restoration: Principles, Processes, and Practices USDA 2008

## Slide 11: A Non-Impaired, Riparian Stream Corridor
Stable
Dissipates energy
Controls flooding
Intercepts pollutants
Facilitates recharge
Provides multiple types of habitats
Highly resilient to storm flows
Stream Corridor Restoration: Principles, Processes, and Practices USDA 2008

## Slide 12: Loss of Stream Channel Resiliency
Often triggered by basic clearing, filling or alteration of riparian vegetation.
Ecosystem becomes less stable.
Results in ecological impairments to adjacent waterway.
Stream Corridor Restoration: Principles, Processes, and Practices USDA 2008

## Slide 13: Evidence of Damaged Riparian Buffer

## Slide 14: How Land Development Impacts Riparian Buffers
Altered hydrology (too much or too little water)
Altered hydraulics (increased flow rates)
Physical damage (clearing and filling)
Disturbance increases invasive plant colonization
Increased water temperature due to clearing and various types of discharges
Impacted water quality (increased pollutant loading)
Ecological impacts (result of all of the above)
Societal impacts (result of all of the above)

## Slide 15: “What Goes Around Comes Around”
Clearing and Filling
Altered Hydrology, Erosion, Thermal Pollution
Increased NPS Pollution
Degraded Water Quality and Habitat
Watershed Development
Loss of Ecological Services and Functions

## Slide 16: Fishery Impacts
Impaired riparian buffers directly linked to compromised fishery
Loss of canopy increases heating of stream, leading to thermal impacts and altered biological community
Loss of canopy and riparian vegetation affects availability and diversity of food1 , aquatic insects…critical for young fish
Decreased woody debris habitat used by fish, invertebrates and amphibians
Decreased stream bank stability = more sedimentation = occluded/ smothered fish and aquatic insect habitat
Increased rate of eutrophication
Decreased baseflow due to loss of flood storage
1 – L. Albertson, V. Ouellet and M. Daniels. 2018. J Freshwater Ecol. 33:1, 195-201

## Slide 17: Watershed Development and Stream and Riparian Area Degradation
As per Schueler, 1992
Stable
Impacted
Degraded

## Slide 18: Here’s What a Little Bit of Runoff Can Do!

## Slide 19
Notes: Meander #1 was a vertical bank just behind the backstop of a ballfield. A hiking/running trail paralleled the stream in close proximity.
Flow did not go out of bank in this bend until it entered the woods.

## Slide 20
Notes: Deep and severely cut banks

## Slide 21: How To Avoid These Problems
Do not fill or disturb riparian buffers.
Do not remove vegetation or mow down riparian buffers.
Practice good stormwater management…reduce volume of runoff, promote recharge and mitigate peak flow related impacts.
Protect canopy.
Replace invasive species with native species.
Deer management.

## Slide 22: Restoration Design
With correct data in-hand, proceed with a design that stratifies restoration goals and is sustainable…work with site and with nature.
Important not to “force fit” a solution. Make sure that the solution is backed by technically strong data.
Overall, the design needs to make sense from an ecological perspective and is consistent with site characteristics and natural attributes.
Too often the projected end-result is not in keeping with native conditions. Decreases success and sustainability of restoration effort.

## Slide 23: In Summary
Riparian buffers provide a variety of ecological services and functions.
Importance of riparian buffers reflected in rules and laws that protect these areas from disturbance.
Importance of riparian buffers reflected in scientific literature.
Value of riparian buffers often underestimated.
Relationship to healthy, vibrant stream ecosystem misunderstood.

## Slide 24: In Summary
Riparian buffers subject to wide array of impacts:
  Agriculture
  Logging
  Land development
  Land maintenance (mowing and clearing of vegetation)

## Slide 25: In Summary
What can be done to promote healthy riparian buffers:
  Don’t fill or disturb riparian buffers.
  Don’t remove or mow down riparian vegetation.
  Practice good stormwater management…reduce runoff volume, recharge, and mitigate peak flow related impacts.
  Protect and enhance riparian tree canopy.
  Replace invasive species with native species.
  Control and manage deer.

## Slide 26: In Summary
Sustainable riparian restoration entails “designing with nature”
Based on “solid” physical, hydrologic, hydraulic, geomorphic data
Reflects understanding of native ecology

## Slide 27: In Summary
A Healthy Riparian Buffer =
A Healthy Stream
Healthy Streams = Healthy Barnegat Bay

## Slide 28
Thank You
Stephen J. Souza, Ph.D.